## Slide 1: Assignment - 4
Computational Electromagnetics
What happens to an EM wave passing through a slab?

## Slide 2: A dielectric slab has following characteristics
1 foot thick
Relative permeability = 2
Relative permittivity = 6

## Slide 3: The following problem is to be solved
Calculate transmittance and reflectance from 0 to 1 GHz signal frequencies.

## Slide 4: Fiddle with the geometry to make it symmetric
εr=1, μr=1,σ=0
εr=1, μr=1,σ=0
εr=6, μr=2
ABC
ABC
TF/SF
Source
Record reflection E(t)
Record Transmission E(t)

## Slide 5: Explain in detail how you calculated the following
Grid spacing
Size of the grid itself
Vacuum padding to left and right dimensions
Time step computation
Source parameters (temporal parameters)
Total number of time steps
Expression for Esource and Hsource

## Slide 6: Lets analyze in the spectral domain
Calculate R(f)=(FFT(Ereflected(t))/FFT(Esource)))2
Calculate T(f)=(FFT(Etransmitted(t))/FFT(Esource)))2
Plot them. Add them together and check for energy conservation.