## Slide 1: Assignment - 5
Computational Electromagnetics
Simple applications to gain confidence and correlate with undergraduate theory

## Slide 2: Problem definition
A radome is being designed to protect an antenna operating at 2.4 GHz. For mechanical reasons, it must be constructed from 1 ft thick plastic with dielectric constant of 12 and relative permeability of 1. How would you modify the design to maximize the transmission through the radome? Simulate the design using 1D TF/SF FDTD.

## Slide 3: Lets simplify it a little bit to understand more
εr=1, μr=1,σ=0
εr=1, μr=1,σ=0
εr=12, μr=1
1 foot wide
ABC
ABC
TF/SF
Source
Record reflection E(t)
Record Transmission E(t)

## Slide 4: You need to modify it to
εr=1, μr=1,σ=0
εr=1, μr=1,σ=0
εr=12, μr=1
1 foot wide
ABC
ABC
TF/SF
Source
Record reflection E(t)
Record Transmission E(t)
ε2
ε2
Thickness d2
Thickness d2

## Slide 5: Some inputs to solve the problem
The permittivity of the orange layers in the previous slide should be the geometric mean of vacuum permittivity (1) and plastic (radome) permittivity (12). The square root of this should give you refractive index n2.
The thickness of the layers d2 should be obtained from λ0/4n2

## Slide 6: Lets analyze in the spectral domain
Calculate R(f)=(FFT(Ereflected(t))/FFT(Esource)))2
Calculate T(f)=(FFT(Etransmitted(t))/FFT(Esource)))2
Plot them. Add them together and check for energy conservation. What happened at 2.4 GHz? What happens at other wavelengths?